## Slide 1: UART
BY SRAVANTHI
CHIPWEAVE TECHNOLOGIES PVT LMD

## Slide 2: Introduction
UART(Universal Asynchronous Receiver/Transmitter)​
Used for serial communication​
It is two wire communication protocol​
One wire for transmission​
Second wire for reception​
There is no clock for UART
Timing is agreed using baud rate
Uses start and stop bits for synchronization

## Slide 3: UART Communication – Frame Structure​
Data is transferred bit-by-bit using a predefined frame format​
A UART frame consists of:​
Start Bit
Data Bits (5–9 bits, typically 8)​
Parity Bit (Optional)​
Stop Bit​

## Slide 4: Features
UART uses asynchronous communication without a shared clock.
It supports full-duplex data transfer using TX and RX lines.
Data framing is configurable (start bit, data bits, parity, stop bits).
Communication speed is set by a programmable baud rate.
It provides basic error detection like parity and framing errors.
UART is simple, low-cost, and widely used in embedded systems

## Slide 5: Registers
Name​ | Width​ | Access​ | Description​
Receiver Buffer​ | 8​ | R​ | Receiver FIFO output​
Transmitter Holding Register (THR)​ | 8​ | W​ | Transmit FIFO input​ ​
Interrupt Enable Register (IER)​ | 8​ | RW​ | Enable/Mask interrupts generated by the UART​
Interrupt Identification Register (IIR)​ | 8​ | R​ | Provides interrupt source information​ ​
FIFO Control Register (FCR)​ | 8​ | W​ | Controls FIFO options​
Line Control Register (LCR)​ ​ | 8​ | RW​ | Controls line configuration​ ​ ​
Modem Control Register (MCR)​ | 8​ | W​ | Controls modem signals​

## Slide 6
Name​ | Width​ | Access​ | Description​
Line Status Register (LSR)​ | 8​ | R​ | Provides line status information​
Modem Status Register (MSR)​ | 8​ | R​ | Modem Status Register (MSR)​ ​

## Slide 7: Interrupt Enable Register (IER)​
This register enables or disables interrupt generation by the UART
Bit #​ | Access​ | Description​ | 
0​ | RW​ | Received Data Available Interrupt​ 0 = Disabled,1 = Enabled​ | 
1​ | RW​ | Transmitter Holding Register Empty Interrupt​ 0 = Disabled,1 = Enabled​ | 
2​ | RW​ | Receiver Line Status Interrupt​ 0 = Disabled,1 = Enabled​ | 
3​ | RW​ | Receiver Line Status Interrupt​ 0 = Disabled,1 = Enabled​ | 
7-4​ | RW​ | Reserved (Must be written as logic 0)​ | 

## Slide 8: Interrupt Identification Register(IIR)
The IIR enables the programmer to retrieve what is the current highest priority pending interrupt.​
Bit 3​ | Bit 2​ | Bit 1​ | Priority​ ​ | Interrupt Type​ | Interrupt Source ​ | Interrupt Reset Control ​
0​ | 1​ | 1​ | 1st​ | Receiver Line Status​ | Parity, Overrun or Framing errors or Break Interrupt ​ | Reading the Line Status Register ​
0​ | 1​ | 0​ | 2nd​ | Receiver Data available​ | FIFO trigger level reached ​ | FIFO drops below trigger level ​
1​ | 1​ | 0​ | 3rd​ | Timeout Indication​ | RX FIFO has data​ No new data received or read for 4 character times​ ​ | Reading from the FIFO (Receiver Buffer Register)​
0​ | 0​ | 1​ | 4th​ | Transmitter Holding Register empty​ | Transmitter Holding Register Empty ​ | Writing to the Transmitter Holding Register or reading IIR. ​
0​ | 0​ | 0​ | 5th​ | Modem Status​ | CTS, DSR, RI or DCD.​ | Reading the Modem status register.​

## Slide 9: FIFO Control Register (FCR)​
The FCR allows selection of the FIFO trigger level (the number of bytes in FIFO required to enable the Received Data Available interrupt).​
Bit | Access ​ | Description ​
0​ | W​ | Ignored (Used to enable FIFOs in NS16550D). Since this UART only supports FIFO mode, this bit is ignored.​
1​ | W​ | Clears Receiver FIFO​ Writing 1 → clears RX FIFO and resets its internal logic​ Shift register not cleared, i.e., the byte currently being received continues normally​
2​ | W​ | Clears Transmitter FIFO​ Writing 1 → clears TX FIFO and resets its logic​ Shift register not cleared, so the byte currently being transmitted continues​ ​
5-3​ | W​ | Ignored​
7-6​ | W​ | Define the Receiver FIFO Interrupt trigger level ‘00’ – 1 byte ‘01’ – 4 bytes ‘10’ – 8 bytes ‘11’ – 14 bytes ​

## Slide 10: Line Control Register (LCR)​
The line control register allows the specification of the format of the asynchronous data communication used.​
Bit ​ ​ | Access​ | Description​
1-0​ | RW​ | Select number of bits in each character​ ‘00’ – 5 bits, ‘01’ – 6 bits, ‘10’ – 7 bits ‘11’ – 8 bits ​
2​ | RW​ | Specify the number of generated stop bits​ '0' - 1 stop bit​ '1' - 1.5 stop bits (only if 5-bit data)​ '1' - 2 stop bits (for 6/7/8-bit data)​ ​
3​ | RW​ | Parity Enable​ ‘0’ – No parity ​ ‘1’ – Parity bit If enabled:​ Transmitter adds parity bit​ Receiver checks parity bit​ ​

## Slide 11: Line Control Register (LCR)​
Bit ​ ​ | Access​ | Description​
4​ | RW​ | Even Parity Select​ Selects odd or even parity (only valid if parity enabled).​ '0' - Odd parity​ '1' - Even parity​
5​ | RW​ | Stick Parity​ Forces parity bit to a fixed value.​ ‘0’ – Stick Parity disabled ​ ‘1’ - Stick parity enabled​
6​ | RW​ | Break Control​ Forces TX line to logic 0 continuously.​ '0' - Normal operation​ '1' - TX line forced LOW (Break condition)​ ​
​7 | ​RW | ​Divisor Latch Access bit. ​ ‘1’ – The divisor latches can be accessed ​ ‘0’ – The normal registers are accessed​

## Slide 12: Modem Control Register (MCR)​
Modem Control Register (MCR) controls handshaking signals between UART and a modem ​
Bit # ​ ​ | Access​ | Description​
0​ | W​ | DTR (Data Terminal Ready) Control Signal​ '0' - DTR output = 1 (UART is ready)​ '1' - DTR output = 0​
1​ | W​ | RTS (Request To Send) control signal​ '0' - RTS output = 1(UART asks Modem) ​ '1' - RTS output = 0​
2​ | W​ | Out1. In loopback mode, connected Ring Indicator (RI) signal input.
3​ | W​ | Out2. In loopback mode, connected to Data Carrier Detect (DCD) input.​

## Slide 13: Modem Control Register (MCR)​
Bit ​ | Access​ | Description​
4​ | W​ | Loopback mode​ ‘0’ – normal operation ​ ‘1’ – loopback mode. When in loopback mode, UART tests itself​ No external modem needed​ Transmitter output internally connected to receiver input​ The following connections are made:​ DTR -> DSR ​ RTS -> CTS ​ Out1 ->RI​ Out2 -> DCD​
7-5​ | W​ | Ignored​

## Slide 14: Line Status Register (LSR) ​
Line Status Register (LSR) tells the current status of UART transmission and reception:​
Bit​ | Access​ | Description​
0​ | R​ | DR (Data Ready)​ Indicates received data availability.​ '0' - No data in RX FIFO​ '1' - At least one byte is available in RX FIFO​ ​
1​ | R​ | OE (Overrun Error)​ RX FIFO overflow detection.​ '1' - FIFO full and new data arrived → data loss​ '0' - No overrun​
2​ | R​ | PE (Parity Error)​ Parity check error detection.​ '1' - Parity error in received character​ '0' - No parity error​

## Slide 15: Line Status Register (LSR) ​
BIT | Access | Description
3​ | R​ | FE (Framing Error)​ Stop-bit error detection​ '1' - Stop bit is invalid or missing​ '0' - Stop bit correct​
4​ | R​ | BI (Break Interrupt)​ Detects long LOW condition on RX line.​ '1'- Line held LOW longer than one frame​ '0' - No break condition​
5​ | R​ | Transmit FIFO is empty. ​ TX FIFO status.​ '1' - TX FIFO empty​ '0' - TX FIFO has data​
6​ | R​ | Transmitter Empty indicator.​ '1' - TX FIFO and shift register empty​ '0' - Transmission still in progress​
7​ | R​ | Error in FIFO ,Error summary bit.​ '1' - At least one error in RX FIFO(Parity error, Framing error ,Break error)​ '0' - No errors​

## Slide 16: Modem Status Register (MSR) ​
Current state of modem control lines​
Whether those signals have changed since the last read​
Bit | Access ​ | Description ​
0​ | R​ | DCTS (Delta Clear To Send)​ Detects change in CTS signal.​ '1' - CTS line changed (0→1 or 1→0)​ '0' - No change​
1​ | R​ | DDSR (Delta Data Set Ready)​ Detects change in DSR signal.​ '1' - DSR line changed​ '0' - No change​
2​ | R​ | TERI (Trailing Edge Ring Indicator)​ Detects falling edge of RI signal.​ '1'- RI changed from HIGH → LOW​ '0' - No falling edge​ ​

## Slide 17: Modem Status Register (MSR) ​
BIT | Access | Description
3​ | R​ | DDCD (Delta Data Carrier Detect)​ Detects change in DCD signal.​ '1' - DCD line changed​ '0' - No change​
4​ | R​ | Complement of the CTS input or equals to RTS in loopback mode. ​
5​ | R​ | Complement of the DSR input or equals to DTR in loopback mode. ​
6​ | R​ | Complement of the RI input or equals to Out1 in loopback mode. ​
7​ | R​ | Complement of the DCD input or equals to Out2 in loopback mode. ​

## Slide 18: UART vs SPI vs I2C
parameter​ | UART​ | SPI​ | I2C​
clock​ | No (Asynchronous)​ | synchronous​ | synchronous​
wires​ | 2​ | 4​ | 2​
speed​ | 1-2mbps​ | 10-100mbps​ | 3.4mbps​
Addressing​ | no​ | Limited(cs)​ | yes​
communication​ | Point –to-point​ | Master-slave​ | Master-slave​
Use case​ | Gps module bluetooth​ | displays​ | sensors​